## Slide 1
Status Report
Week 8
JetRover Autonomous Retrieval
Andy Estrada and Riley Barclay

## Slide 2
Project Goal & Starting Point
Goal: find an object, drive to it, pick it up, and bring it back to the starting location.
Manual driving had previously worked on the robot.
Existing code supported color detection, approach, and basic arm actions.
This week focused on software; the robot was unavailable.
2

## Slide 3
Work Completed This Week
Reviewed the repository and robot driver interfaces.
Implemented a mission that saves the starting position and heading.
Added odometry-based return navigation and placement at home.
Updated configuration, launch options, and operating instructions.
3

## Slide 4
Updated Mission Flow
Save home > Search > Align > Approach > Pick Confirm pickup > Return home > Place > Complete
Camera detection tracks a red, green, or blue object.
Depth readings guide alignment and approach to pickup range.
The arm lifts the object into a carrying pose.
The robot returns to its saved pose before placing it.
4

## Slide 5
Control & Reliability Improvements
Added explicit start/stop controls and mission status reporting.
Added sensor freshness checks and movement timeouts.
Removed forward movement without valid depth.
Made arm actions responsive to stop requests; added gripper limits and a chassis command timeout.
5

## Slide 6
Current Status & Limitations
Initial implementation is complete; no builds or tests have been run.
Pickup confirmation requires an operator by default.
Automatic return can be enabled, but pickup then remains unverified.
Return assumes a clear route. Obstacle avoidance and physical return accuracy remain unresolved.
6

## Slide 7
Next Steps
Install the mission package and updated chassis driver on the robot.
Confirm sensor topics and camera/depth registration.
Calibrate pickup distance, arm poses, and gripper settings.
Check stopping and short return trips, then run a supervised retrieval mission.
7